## Slide 1: StableBuffer: Optimizing Write Performance for DBMS Applications on Flash Devices
Paper by: Yu Li, Jianliang Xu, Byron Choi, and Haibo Hu
Department of Computer Science
Hong Kong Baptist University
Slides and Presentation By: Justin Weaver

## Slide 2: Introduction
Flash devices offer…
  Much faster random reads compared to HDDs
  Lower power consumption
But random writes can be very slow
Proposed solution called StableBuffer
Takes advantage of efficient write patterns
Implemented as DBMS buffer manager add-on
No need for firmware or OS driver updates

## Slide 3: Why So Slow?
Why are random writes to NAND flash so slow?
Only empty cells can be written to
Writes at page level, but erases operate on blocks
Overwrite operation: read, erase, modify, write

## Slide 4: The StableBuffer Solution
Execute all writes to empty “slots” in a pre-allocated buffer on the flash device
Take note of the writes’ actual destinations and look for efficient write patterns
Flush the buffer by writing the discovered patterns to their actual locations

## Slide 5: Efficient Write Patterns
Sequential Writes – consecutive addresses
Focused Writes – addresses within a specific range
Partitioned Writes – mix of sequential writes to several areas

## Slide 6: Design Challenges
How should the space inside of the StableBuffer be managed?
How should efficient write patterns be recognized without too much overhead?
Which write patterns should be flushed to their destinations, and when should this happen?

## Slide 7: Data Structures
StableBuffer
  Pre-allocated area on the flash device
  Broken into slots, each the size of a page
  Example: 4MB SB, 4KB pages  1,024 slots
Translation Table
  In-memory table that maps actual destinations with slot numbers
  Example entry: <0x1234ABCD, 42>
  Implemented as hash table, key is destination address
Bitmap for Free Slots
  “1”  empty , “0”  occupied
  Free slot pointer points to next open slot
Metadata added to pages for fault tolerance

## Slide 8: StableBuffer Manager
Reader
Writer
Flush Manager

## Slide 9: Reader
Checks to see if page is in SB first
  If it is, read it from the SB
  If not, read it from the actual destination
Paper claims the overhead is negligible because of hashing

## Slide 10: Writer
Overwrite page in table if destination is already there, then return
OR ...
Invoke flushing if free slot pointer is null
Write page to free slot
Update table and bitmap
Update free slot pointer

## Slide 11: Flush Manager
Write pattern recognition
  On-Demand
  Incremental
Pattern Flush Strategies
  Passive
  Proactive

## Slide 12: On-Demand vs. Incremental
On-Demand
  Finds efficient write patterns upon request
  Scan on sorted destination addresses finds sequential and partitioned patterns
  Sliding window on sorted addresses finds focused area patterns
Incremental
  Maintains pattern information; updated after every write
  Maintain set of Si = (addrmin, addrmax) to find sequential writes
  Maintain set of Pl where each entry points to all Si with size l; each Pl is a candidate partitioned write pattern
  Maintain set of Fi = (addrmin, addrmax, setaddr) where setaddr is a set of addresses between min and max; each Fi is a candidate focused write pattern

## Slide 13: Passive vs. Proactive
Passive
  Flushes pages when there are no open slots
  Triggers on-demand pattern recognition OR chooses incrementally generated patterns
  Chooses to flush the longest instance that is expected to be written fastest
Proactive
  Flushes pages during any write operation when qualified to do so
  Requires incremental pattern recognition
  Runs in the background, detecting good efficient write patterns
  Checks if maintained patterns are qualified for flushing
  Qualified patterns have a threshold value higher than θx where x is one of the three write patterns
  θseq = lmin / l θpar = θseq * T par / T seq θfocus = θseq * T focus / T seq

## Slide 14: Experiment Setup
Three flash devices
  16GB SSD
  8GB USB flash drive
  8GB SDHC card
Three StableBuffer configurations
  Ondemand+Passive
  Incremental+Passive
  Incremental+Proactive
TPC-C benchmark on PostgreSQL 8.4

## Slide 15: Throughput and Response Time
All measurements outperform direct method
SD card has poor performance with incremental+proactive
Incremental+passive and ondemand+passive perform the best

## Slide 16: Other Tests
SD card performs very poorly in parallel write test
USB flash drive and SD card are clearly IO bound, not CPU bound

## Slide 17: StableBuffer Size
Best performance achieved when StableBuffer size was set to 4MB for this particular drive

## Slide 18: Paper Conclusions
Using the StableBuffer DBMS add-on, random write performance on flash memory was shown to dramatically increase
No firmware or OS driver updates were needed

## Slide 19: Questions
Comprehension questions?
...
Presentation questions...
  Does optimal performance rely too heavily on the need to benchmark each specific device model first?
  Could developments in firmware and/or OS drivers make an add-on like StableBuffer no longer necessary?
  USB flash drives and SD cards would probably never be used for DBMS storage; why not just test several different SSD models instead?
  Could OS support for the TRIM command help with random write performance within a DBMS?